## SPECIFICATION

# COMBO’BEDKIT

VERTICAL BED HEAD PROTECTION – 750 MM HIGH

- Description: double vertical bed head protection (Combo’Bedkit as manufactured by SPM) from slightly textured (Optimixt grain as manufactured by SPM) and antibacterial PVC achieving Bs2d0 fire rating with solid colour. It comprises vertical PVC profile to snap-fix onto aluminium rail with 2 end pieces. It projects 75 mm (on rubber absorbers) or 200 mm (on metal extenders), is 750 mm high and 100 mm wide. These parts ﬁt together on 2 rubber absorbers (25 mm thick) or on 2 metal extenders (150 mm long).

- Environment: no heavy metals and no substance potentially subjected to any REACH restriction are used in its manufacture, nor PBT/BPA. The calcium-zinc thermal stabilization process is used. The emission level of volatile substance in inside air has been tested according to ISO 16000-6 and is very low (A+) according to the French regulation (23 March 2011 nr 2011-321 Decree and 19 April 2011 Order). 100% of the product are recyclable.

- Colour: selected by architects from manufacturer’s standard range.

- Installation method: ﬁxes aluminium rail onto the rubber absorbers or the metal extenders then the end pieces and snap-ﬁxes onto the PVC proﬁle.